KOMEDIA – STUDIO

Venue Specifications

CAPACITY

The Studio at Komedia is an intimate small scale venue. Capacity is 80-100 seated (depending on layout and stage size) and 140 standing (additional guest list available on top of standing events).

STAGE

The stage is fully draped in black wool serge curtains and is 340cm deep by 380cm wide with the steel deck extension in place and 240cm deep and 380cm wide without the extension. The smaller stage can increase the rowed capacity slightly depending on layout. Stage floor to ceiling is 2.5m, the stage is 40cm high from the auditorium level.

SPEAKERS

The FOH rig is a pair of D&B C690 full range speakers flown, powered by E-Pac amps and two Noise Control Audio VSB 215 sub-woofer powered by a QSC RMX 2450 amp.

Monitors: 4 way mix, 4 matching DAS audio Action 12’s. 2 x QSC 1200w amps. Extra sends available for IEM’s etc.

FOH SOUND

MIDAS M32 Digital Console

LIGHTING

Chamsys MQ40 console

2 x Zero 88 Betapack-2 dimmers, 15 amp (giving a total 12 x dual inputs).

Onstage Lighting Bars:

2 x Stairville MH – x5- LED Spot (moving heads)

3 x Stairville Mini Stage Par LED – 7x3w

2 x Stairville Par 18 Tri Colour LED 3w

2 x Total Fabrications Par 64’s 300w,

2 x Strand Quartet Fresnels

FOH Lighting Bar:

1 x Strand Cantata Fresnel 1kw – Cool front wash

1 x Harmony Fresnel 1kw – Warm front wash

2 x Strand Quarter Fresnel 650w – General Cover

1 x ETC Source Four 750 Profile – Spotlight

2 x Skytec Par 64 500w (on separate faders) – Audience/colour wash

1 x Strand Quartet Fresnel 650w – Audience/colour wash/ stage wash

2 x Skytec 100w

1 x Mac 250 moving head

Mirror Ball

Sound to Light/Club Lights:

Various Sound to light DJ lanterns and Lazer.

Hazer:

1 x Le Maitre Nuetron XS

AV:

Projector: Acer X1110

Screen: 105 inches / 267 cm (16:9)

Roland Edirol V4 Vision Mixer

MICROPHONES, DI’S AND CABLES:

Please note additional equipment available on advance request:

10 x Shure SM 58’s Microphones

5 x Shure SM 57’s Microphones

Shure PG drum set. (kick mic/3 x drum clips)

2 x PG 56 condenser mics

2 x Senn. e604 clips

1 x Senn e906

9 x DI

All technical equipment is operated from FOH position - approx 4 m from the stage. There are numerous RCD protected double 13amp power sockets at the rear of the stage.

Please contact Lloyd/Dave (Technical Dept.) to discuss any specific needs your event requires.

Telephone: 01273 647101
Email: technical@komedia.co.uk